'****************************************************************

'*  Name    : UNTITLED.BAS                                      *

'*  Author  : [select VIEW...EDITOR OPTIONS]                    *

'*  Notice  : Copyright (c) 2006 [select VIEW...EDITOR OPTIONS] *

'*          : All Rights Reserved                               *

'*  Date    : 7/9/2006                                          *

'*  Version : 1.0                                               *

'*  Notes   : PicBasic Pro program that demonstrates the use    *

'*          : of the Timer 1 interrupt for a real-time clock.   *

'*          :                                                   *

'****************************************************************

DEFINE LOADER_USED 1    ' Needed for bootloader redirect

DEFINE OSC 20           '20 Mhz Resonator

DEFINE LCD_DREG	PORTB	'Define PIC port used for LCD Data lines

DEFINE LCD_DBIT	4	'Define first pin of portb connected to LCD DB4

DEFINE LCD_RSREG PORTB	'Define PIC port used for RS line of LCD

DEFINE LCD_RSBIT 0	'Define Portb pin used for RS connection

DEFINE LCD_EREG	PORTB	'Define PIC prot used for E line of LCD

DEFINE LCD_EBIT	3	'Define PortB pin used for E connection

DEFINE LCD_BITS	4	'Define the 4 bit communication mode to LCD

DEFINE LCD_LINES 2	'Define using a 2 line LCD

DEFINE LCD_COMMANDUS 2000'Define delay between sending LCD commands

DEFINE LCD_DATAUS 100	'Define delay time between data sent.

' Define Assembly Language interrupt handler

DEFINE  INTHAND myint   ' Define interrupt handler

' Establish special variables for assembly interrupts

wsave   VAR     BYTE $20 system	'W storage in bank0

wsave1  VAR     BYTE $a0 system 	' W storage in bank1

wsave2  VAR     BYTE $120 system 	' W storage in bank2

wsave3  VAR     BYTE $1a0 system 	' W storage in bank3

ssave   VAR     BYTE bank0 system	' Status register save

psave   VAR     BYTE bank0 system	' PCLATH register save

TICK	VAR	BYTE bank0	' make sure that the variables are

' in bank 0 if they are to be used

' in the interrupt handler

PRELOAD var byte bank0  ' value for timer preload

seconds VAR BYTE		' Elapsed seconds

minutes VAR byte		' Elapsed minutes

hour    var byte    	' Elapsed hours

minutes = 0			' Preset time to 12:00:00

seconds = 0

hour = 12

preload = $80		' Preset timer to 80 hex

T1CON = $0F		' Turn on Timer1, prescaler = 1, External 32.768Khz

INTCON = $C0	' Enable global interrupts, peripheral interrupts

PIE1 = $01			' Enable TMR1 overflow interrupt

GoTo init 		' jump over the interrupt handler and subroutine

' ********************

' Assembly language interrupt handler

' ********************

Asm		; Tell PicBasic Pro Assembly Commands follow

myint

; Uncomment the following if the device has less than 2k of code space

;movwf	wsave			; Save W

;swapf	STATUS, W	; Swap STATUS to W (swap avoids 						; changing STATUS)

;clrf	STATUS		; Clear STATUS

;movwf	ssave		; Save swapped STATUS

;movf	PCLATH, W		; Move PCLATH to W

;movwf	psave		; Save PCLATH

; Set the high register of Timer1 to cause an interrupt every

; 32768 counts (65536-32768 = 32768 or $8000).

;	movlw	080h			; Prepare to set TMR1 high register

movf    _PRELOAD,W  ; Preload Timer1 for 1 second overflow

movwf	TMR1H		; Set TMR1H to 80h

incf	_TICK,F	; Increment TICK count (number of overflows)

bcf     PIR1, 0	; Clear interrupt flag

movf    psave, W	; restore the state of everything

movwf   PCLATH

swapf   ssave, W

movwf   STATUS

swapf   wsave, F

swapf   wsave, W

retfie   		; Return from interrupt

EndAsm			' End of assembly code

' ***********************

' PicBasic subroutine to update the minutes and seconds variables

' ***********************

get_time:

' Read the timer1 overflows as TICK and then add to the seconds

' variable. Increment Minutes and Hours as necessary.

PIE1 = 0				' Mask the interrupt while we're messing with TICK

seconds = seconds + tick	' Add the accumulated seconds

tick = 0           		' Retain the left-over ticks

PIE1 = $01				' Interrupt on again

minutes = minutes + (seconds / 60)	' Add the accumulated minutes

seconds = seconds // 60		' Retain the left-over seconds

hour = hour + (minutes/60)   	'Add the accumulated hours

minutes = minutes//60   	' Retain the left -over minutes

if hour > 12 then

hour = hour - 12

endif

Return					' Return to the main program

init:

' **************************************************************

' Begin program code here. The time will be updated when you call the

' get_time routine.

' **************************************************************

LCDOut $fe,1		' Clear LCD

main:

GoSub get_time	' Update minutes and seconds

'**** Display the elapsed time ******

LCDOut $fe, 2, DEC2 hour, ":", DEC2 minutes, ":", DEC2 seconds

GoTo main 		' Repeat main loop

End