setpullups pu_on		'PortB Pullups On

stat var byte		'Create variable Status

trisb = %11111111	'RB6 and RB7 input, Rest of

' PORTB Outputs

main

high p8  ' LED On indicating Armed and ready

stat = portb  ' The value of PortB is captured

if stat = $FF then main   'Test for Car, loop back if

'not sensed

if stat = 223 then   'Test if Right Lane won

high 12	' Right LED on

low 13	' Left LED off

goto wait	' Jump to reset loop

elseif stat = 191	'Test if Left Lane won

high 13	' Left LED on

low 12	' Right LED off

goto wait	' Jump to reset loop

else

high 12		' Tie

high 13		' Light both LEDs

goto wait		' Test again

endif

wait

low p8			' Armed LED off

if in9 = 1 then wait	' Wait for rearmed

' switch press

low 12			' Reset LEDs

low 13

goto main