;*******************************************************************************************

;*****************   PROGRAM: Slot car code                 *******************************************

;*****************   WRITEN BY: JOHN MOUTON       *******************************************

;*****************        DATE: 9-17-07                              *******************************************

;********************************************************************************************

LIST	p=12f683		         ; DIRECTIVE TO DEFINE PROCESSOR

#INCLUDE	<p12F683.inc>	     ; PROCESSOR SPECIFIC VARIABLE DEFINITIONS

__CONFIG _MCLRE_OFF & _WDT_OFF & _INTRC_OSC_NOCLKOUT & _CP_OFF & _CPD_OFF &

_FCMEN_OFF & _IESO_OFF & _BOD_ON & _PWRTE_ON

; VARIABLES

CBLOCK 0x020

STATUS_TEMP

WORK_TEMP, DELAY, DELAY_COUNTER

DELAY_TIMER, DELAY_COUNTER3

LAP_COUNTER, SECTION_COUNTER, LED_COUNT

DELAY_COUNTER2, LAP_COUNTER2, SECTION_SENSOR

ENDC

PAGE

BANK1                MACRO                 ; BANK 1 SELECTION MACRO.

BSF  STATUS, RP0

ENDM

BANK0               MACRO                 ; BANK 0 SELECTION MACRO.

BCF  STATUS, RP0

ENDM

DUTY_CYCLE  MACRO   A             ; DUTY CYCLE SELECTION MACRO.

MOVLW	A

MOVWF	CCPR1L

ENDM

DELAY_TIME   MACRO   A		      ; GENERATES "A" MULTIPLE 50 MS DELAYS

MOVLW	A

BANKSEL DELAY_COUNTER3

MOVWF	DELAY_COUNTER3

CALL	DELAY_MS

ENDM

ORG	0x0000				      ; PROCESSOR RESET VECTOR

BANK0

GOTO	INITIALIZE_REGISTERS

ORG	0x0004				      ; INTERRUPT VECTOR LOCATION

RETFIE

INITIALIZE_REGISTERS

BANKSEL CMCON0

MOVLW	B'00000111'

MOVWF	CMCON0			      ; THIS WILL TURN THE COMPARATOR OFF.

BANKSEL INTCON

MOVLW	B'00000000'

MOVWF	INTCON                ; SETTING THE INTCON REG TO ENABLE THE TMR0 OVERFLOW.

BANKSEL ANSEL

CLRF	ANSEL			      ; DISABLE THE ANALOG INPUTS, DISABLES THE ANALOG SELECT REG.

BANKSEL WPU

CLRF	WPU				      ; DISABLE THE WEAK PULLUPS

BANKSEL TRISIO

MOVLW	B'00100000'		      ; TRISIO5 IS SET AS AN INPUT AND

MOVWF	TRISIO

BANKSEL OPTION_REG

MOVLW	B'11010001'

MOVWF	OPTION_REG

BANKSEL OSCCON

MOVLW	B'01110001'

MOVWF	OSCCON			      ; SETS THE INTERNAL OSCILLATOR TO 8MHZ.

BANKSEL OSCTUNE

CLRF    OSCTUNE

BANKSEL T2CON

MOVLW   B'00000111'

MOVWF   T2CON

BANKSEL TMR0

CLRF	TMR0

BANKSEL GPIO

CLRF	GPIO

CLRF	DELAY

CLRF    DELAY_COUNTER2

CLRF	DELAY_COUNTER

BANKSEL DELAY_TIMER

CLRF    DELAY_TIMER

BANKSEL SECTION_COUNTER

CLRF    SECTION_COUNTER

MOVLW   01H

MOVWF   SECTION_COUNTER

;**************************************************************************************

;***************** PWM  ***************************************************************

;**************************************************************************************

PWMSU						             ; PWM SET-UP

BANK1

;**************************************************************************************

MOVLW	   .100

MOVWF	   PR2                       ; SETS PWM PERIOD.

;***************************************************************************************

BANK0

MOVLW	   B'00000101' ; TIMER2 CONTROL REG. THIS SETS PRESCALER AND POSTSCALER.

MOVWF	   T2CON

;***************************************************************************************

BANKSEL    CCP1CON

MOVLW	   B'00001100'

MOVWF	   CCP1CON			     ; PWM MODE IS SELECTED.

BANKSEL    CCPR1L

MOVLW      B'00010011'

MOVWF      CCPR1L

;****************************************************************************************

;***************** START OF PROGRAM. ****************************************************

;########################################################################################

START

BANKSEL GPIO

BSF     GPIO, 2                  ; GP2 GOES LOW THUS SW2 IS OFF

BCF     GPIO, 4                  ; GP4 GOES HIGH THUS SW1 IS ON

;**************************************************

DUTY_CYCLE     .34			             ; CHANGE DUTY CYCLE HERE.

;**************************************************

WHERE_AM_I

;******************************************************************************************

;********   JUMP TABLE FOR THE DIFFERENT SECTIONS OF TRACK. *******************************

;*************************** HERE AS THE CAR READS THE IR VALUE FROM THE TRACK, THIS

; SUBROUTINE WILL USE SECTION COUNTER TO DETERMINE WHERE THE

; CAR IS ON THE TRACK AND JUMP TO THE SPECIFIC SET OF

; INSTRUCTIONS FOR THAT PARTICULAR SECTION OF TRACK.

MOVF      SECTION_COUNTER, W

ANDLW     0x07

ADDWF     PCL, F

GOTO      START 		   ; ZERO CONDITION. THIS WILL NOT OCCUR, BUT JUST IN CASE.

GOTO      TRACK_SECTION_1

GOTO      TRACK_SECTION_2

GOTO      TRACK_SECTION_3

GOTO      TRACK_SECTION_4

;******************************************************************************************

;******************  TRACK SECTIONS  ******************************************************

;******************************************************************************************

TRACK_SECTION_1		; STARTING LINE STRAIGHT AWAY. GO FORWARD AND KEEP

; READING THE TRACK.

INCF      SECTION_COUNTER, F	 ; INCREMENT SECTION_COUNTER

;***************************************************

DUTY_CYCLE      .34					 ; CHANGE DUTY CYCLE HERE.							                              ;***************************************************

CALL      TEST_GPIO5

GOTO      WHERE_AM_I

TRACK_SECTION_2       			            ; LEFT 90 DEGREE TURN ( TURN 1 ). THUS BRAKE INTO THE

BANKSEL   GPIO			            ; TURN AND HIT THE GAS OUT OF THE TURN.

CALL      BRAKE   		                         ; **************************************************

DELAY_TIME  .90			            ; CHANGE DELAY TIME HERE.

CALL      FORWARD			            ; **************************************************	DUTY_CYCLE	.30		            ; CHANGE DUTY CYCLE HERE.									                         ; **************************************************

CALL      TEST_GPIO5

INCF      SECTION_COUNTER, F	 ; INCREMENT SECTION_COUNTER

GOTO      WHERE_AM_I 	              ; THEN POWER OUT (FORWARD) OF THE TURN.

TRACK_SECTION_3		      ; BACK STRAIGHT AWAY. GO FORWARD AND KEEP READING THE TRACK.

INCF      SECTION_COUNTER, F	 ; INCREMENT SECTION_COUNTER

;*************************************************

DUTY_CYCLE	.34			                    ; CHANGE DUTY CYCLE HERE.									                                 ; ************************************************

CALL      TEST_GPIO5

GOTO      WHERE_AM_I

TRACK_SECTION_4		 ; SECOND LEFT 90 DEGREE TURN ( TURN 2 ). THUS BRAKE INTO THE

; TURN AND HIT THE BRAKES ON THE WAY OUT OF THE TURN AFTER

; COMPLETING 4 LAPS.

BANKSEL   GPIO

CALL      BRAKE

; *************************************************

DELAY_TIME  .90				          ; CHANGE DELAY TIME HERE.

CALL      FORWARD				    ; *************************************************

DUTY_CYCLE  .30 				          ; CHANGE DUTY CYCLE HERE.

; *************************************************

CALL    TEST_GPIO5

GOTO      RESET

;##################################################################################################

;**************************************************************************************************

;**************  SUBROUTINE FOR TESTING THE TRACK  ********************************************

;**************************************************************************************************

; THIS SUBROUTINE WILL SCAN/TEST THE TRACK LOOKING FOR THE IR SENSORS. THESE SENSORS WILL

; THEN BE USED TO DETERMINE WHAT SECTION OF TRACK THE CAR IS ON.

TEST_GPIO5					; TESTS FOR THE PHOTO TRANSISTOR

BANKSEL LED_COUNT

CLRF    LED_COUNT		; I AM USING A 10 COUNT TO INSURE THAT THE HIGH/LOW CHANGE

MOVLW	.10		; REALLY CHANGES, THUS DEBOUNCE IS NOT AN ISSUE.

MOVWF	LED_COUNT

TEST_LOW

BANKSEL GPIO

BTFSC	GPIO,5			; AS THE CAR PASSES OVER THE SENSOR THE TRACK SIGNAL GOES LOW.

GOTO	TEST_GPIO5		; MAKING SURE IT IS READ 10 TIMES LOW IN A ROW.

DECF	LED_COUNT, F

BTFSS	STATUS, Z

GOTO	TEST_LOW

OVER_LED				; AFTER READING LOW 10 TIMES IN A ROW, IT KNOWS IT IS OVER THE

BANKSEL LED_COUNT	; IR LED SENSOR.

MOVLW	.20		; GP5 HAS BEEN READ LOW 10 TIMES

MOVWF	LED_COUNT

TEST_HIGH				; NOW IT WILL SCAN FOR THE SIGNAL TO GO HIGH.

BANKSEL GPIO

BTFSS	GPIO,5

GOTO	OVER_LED		; MAKING SURE IT IS READ 20 TIMES HIGH IN A ROW

DECF	LED_COUNT, F

BTFSS	STATUS, Z

GOTO	TEST_HIGH		; GP5 HAS BEEN READ HIGH 20 TIMES

RETURN			; WE HAVE JUST PASSED THE IR LED SENSOR.

;******************************************************************************************

;*****************  DELAY LOOP  **********************************************************

;******************************************************************************************

DELAY_MS					; GENERATES A 1MS DELAY LOOP

BANKSEL	DELAY

MOVLW	.200

MOVWF	DELAY

PAUSE

NOP						;1

NOP						;2

NOP						;3

NOP						;4

NOP						;5

NOP						;6

DECF	DELAY, F		;7

BTFSS	STATUS, Z		;8

GOTO	PAUSE			;9 10

DECF	DELAY_COUNTER3, F

BTFSS	STATUS, Z

GOTO 	DELAY_MS

LEAVE_DELAY

RETURN

;********************************************************************************************

;****************  FOWARD SUBROUTINES  ***************************************************

;********************************************************************************************

FORWARD

BANKSEL GPIO

BSF     GPIO, 2                  ; GP2 GOES LOW THUS SW2 IS OFF

BCF     GPIO, 4                  ; GP4 GOES HIGH THUS SW1 IS ON

RETURN

;*********************************************************************************************

;*****************  BRAKE SUBROUTINE  ******************************************************

;*********************************************************************************************

BRAKE

DUTY_CYCLE  .00

BANKSEL   GPIO

BSF       GPIO, 4                ; GP4 GOES HIGH THUS SW1 IS ON

BCF       GPIO, 2                ; GP2 GOES LOW THUS SW2 IS OFF

RETURN

;*********************************************************************************************

;***************  SECTION RESET SUBROUTINE   ***********************************************

;*********************************************************************************************

RESET						         ; STARTING AT THE BEGGINING OF THE TRACK.

BANKSEL SECTION_COUNTER

CLRF    SECTION_COUNTER

MOVLW   01H				         ; SETS SECTION COUNTER TO 1.

MOVWF   SECTION_COUNTER

GOTO    START

END